## Slide 1: PHITS
Automated execution of PHITS by changing simulation conditions using script files
Multi-Purpose Particle and Heavy Ion Transport code System
Title
Dec 2024 revised
/phits/lecture/advanced/autorun
Notes: PHITS講習会 基礎実習

## Slide 2
Purpose
Learn how to run multiple PHITS simulations at once by changing a certain parameter
Purpose of This Lecture
Analysis of the energy dependence of nuclear reaction
Shielding calculation by changing the target thickness
Calculation of dose conversion coefficient for various irradiation geometries
For example…
Make script file by yourself,
or use “autorun.bat” or “autorun.sh” with icntl = 16

## Slide 3
Contents
Table of Contents
Make your own script files
Use “autorun.bat/sh”
Use [anatally] and ANOVA
Summary

## Slide 4: What is script file?
A text file that consists of series of commands to be executed by command-line interpreter or terminal
Windows: Batch file (*.bat)
*Mac/Linux: Shell script (*.sh)
Grammars of batch file and shell script are similar but different
PHITS is executed by phits.bat or phits.sh in “phits/bin” folder
@echo off
title PHITS: %1
set PHITS_Single_EXE="C:\phits/bin/phits324_win.exe“
…
phits.bat
phits.sh
#!/bin/sh
OMP=1
# OMP = 0 -> OpenMP with default OMP_NUM_THREADS
…
If you want to run a different version of PHITS, you must change the executable file name in the script
*When you create a new shell script, you have to add executable status by “chmod u+x *.sh”

## Slide 5: Exercise 1: Run a script file
Open “Explore” and move to “phits/utility/script/instruction”
Type “cmd” and press “enter” → terminal window is opened
Type “eachrun.bat” in the terminal window and press “enter”
*Simply double-click “eachrun.bat” also works, but terminal window disappears after the execution
Type “cmd” here
Open “Terminal” and move to “phits/utility/script/instruction”
Type “./eachrun.sh” or “eachrun.sh”
If you encounter “command not found”, type “chmod u+x *.sh” to add executable status for all .sh files and try again
To repeat the same command, press “↑” and “enter”*
*If you press “↑” twice, you can go back two-previous command
Mac
Windows

## Slide 6: What is written in eachrun.bat?
1st line: write “PHITS simulation using eachrun.bat” in the terminal
2nd line: write “set:c1[2.3]” into a file named “density.inp”
3rd line: execute PHITS with “phits.inp”
“echo” means write the following message
“>” means “to the following file” (Overwrite if the file exists)
“call” is necessary for running another batch script in a batch script
echo PHITS simulation using eachrun.bat
echo set:c1[2.3] > density.inp
call phits.bat phits.inp
eachrun.bat
echo PHITS simulation using eachrun.sh
echo set:c1[2.3] > density.inp
phits.sh phits.inp
eachrun.sh
Role of each line
Important notices
Example of terminal Window
*To see a batch file, right click the file and “open with” a text editor or “Edit”
*

## Slide 7: phits.inp
Basic setup
20 MeV neutron at (0,0,-10) going to +z-axis
Cylindrical concrete with thickness of 50 cm and radius of 10 cm
[t-track] for calculating the effective dose using multiplier function
Source：
Geometry：
Tally：
Important point
Density of concrete is specified by –c1, which is defined in density.inp
track_rz.eps
[ Cell ]
infl:{density.inp}
1 1 -c1 -10 101 -102
100 0 -999 #1
101 -1 999
…
phits.inp

## Slide 8: Exercise 2
Open eachrun.bat/sh with text editor
Change c1 parameter written in density.inp from 2.0 to 2.3
Save eachrun.bat/sh
Execute eachrun.bat/sh (Press “↑” and “enter” in the terminal)
Change the concrete density from 2.0 g/cm3 to 2.3 g/cm3
echo PHITS simulation using eachrun.bat
echo set:c1[2.3] > density.inp
call phits.bat phits.inp
eachrun.bat
echo PHITS simulation using eachrun.sh
echo set:c1[2.3] > density.inp
phits.sh phits.inp
eachrun.sh
*
*To see a batch file, right click the file and “open with” a text editor
track_rz.eps
slightly increased
↑
↑
↑
0
0

## Slide 9: Exercise 3
Change “c1[2.0]” to “c1[%1]” for Windows, “c1[$1]” for Mac/Linux
Save eachrun.bat/sh
Type “eachrun.bat 3.0” for Windows, “./eachrun.sh 3.0” for Mac/Linux in the terminal
Use variable in the script
echo PHITS simulation using eachrun.bat
echo set:c1[2.0] > density.inp
call phits.bat phits.inp
eachrun.bat
echo PHITS simulation using eachrun.sh
echo set:c1[2.0] > density.inp
phits.sh phits.inp
eachrun.sh
track_rz.eps
%1]
$1]
↓
↓
↓
decreased
%1 indicates the 1st variable specified after eachrun.bat (separated by space)

## Slide 10: Exercise 4
*Backslash is something like in your keyboard
Add commands to “eachrun.bat” or “eachrun.sh” to make a new folder in “eachout” and copy all output files (*.out and *.eps) to the folder
Type “eachrun.bat 2.0” for Windows, “./eachrun.sh 2.0” for Mac/Linux in the terminal
Check eachout/2.0 folder by “explore” or “finder”
Automatically save output files by adding commands to “eachrun.bat/sh”
echo PHITS simulation using eachrun.bat
echo set:c1[%1] > density.inp
call phits.bat phits.inp
mkdir eachout\%1
copy *.out eachout\%1
copy *.eps eachout\%1
eachrun.bat
echo PHITS simulation using eachrun.sh
echo set:c1[$1] > density.inp
phits.sh phits.inp
mkdir -p eachout/$1
cp *.out eachout/$1
cp *.eps eachout/$1
eachrun.sh
“*.out” means all files having the extension of “.out”
Folder name should be separated by
\ (backslash) for batch file*
/ (slash) for shell script
Tips
“-p” after mkdir may not be necessary depending on your environment

## Slide 11: Exercise 5
Open “multirun.bat” for Windows, “multirun.sh” for Mac/Linux by text editor
Copy the 1st line and paste it by 4 times
Change the number from 2.0 to 2.2, 2.4, 2.6, & 2.8, respectively
Type “multirun.bat” for Windows, “./multirun.sh” for Mac/Linux in the terminal
Check the dependence of concrete density on the attenuation factor
Run PHITS with various conditions at once
call eachrun.bat 2.0
call eachrun.bat 2.2
call eachrun.bat 2.4
call eachrun.bat 2.6
call eachrun.bat 2.8
multirun.bat
multirun.sh
./eachrun.sh 2.0
./eachrun.sh 2.2
./eachrun.sh 2.4
./eachrun.sh 2.6
./eachrun.sh 2.8
2.0 g/cm3
2.2 g/cm3
2.4 g/cm3
2.6 g/cm3
2.8 g/cm3

## Slide 12
Contents
Table of Contents
Make your own script files
Use “autorun.bat/sh”
Use [anatally] and ANOVA
Summary

## Slide 13: “autorun.bat” & “autorun.sh” in PHITS
Execute PHITS for various conditions by automatically changing a parameter (ci)
Analyze the dependence of tally results on ci using [anatally] (optional)
Original script files are included in phits/bin folder
How to use?
Make a PHITS input file (e.g. phits.inp) with variable ci
Set “icntl = 16” in the PHITS input file
Make a input file for autorun.bat/sh (e.g. autorun.inp) to specify how to change the variable
Run autorun.bat/sh with the input file
PHITS are iteratively executed until the simulations for all conditions are finished, and the results are moved to ‘1’, ‘2’, ‘3’ … folders in “outfiles”
Similar to “multirun.bat/sh”, but you can automatically change the parameter without the knowledge of batch file / shell script

## Slide 14: Exercise 6
Change “icntl = 16” in phits.inp (script mode)
Type “autorun.bat” for Windows, “./autorun.sh” for Mac/Linux in the terminal*
file=phits.inp $ PHITS input file name
set:c1 $ Variable parameter
c-type=1 $ 1: data point, 2: linear, 3: log interpolation
nc=3 $ Number of data points
2.0 2.3 2.8
autorun.inp
phits.inp
[ Parameters ]
icntl = 16
…
Run PHITS with “file=phits.inp“ by changing “set:c1” by “nc=3” times
The format of “c-type” is similar to that of the tally mesh
Calculated results for c1 = 2.0, 2.3 and 2.8 are moved to “1”, “2”, “3” folders in “outfiles”
Variable can be check by varfile.inp in each folder
Run autorun.bat /autorun.sh
*You can specify the input file name as the 1st variable (e.g. autorun.bat autorun.inp)

## Slide 15: Exercise 7
Change c1 from 2.0 to 2.8 by 0.2 step (nc = 5)
Use c-type = 2 ( linear interpolation)
Minimum & maximum values of c1 can be specified by cmin & cmax
Save “autorun.inp” and run “autorun.bat” or “autorun.sh” with autorun.inp
file=phits.inp $ PHITS input file name
set:c1 $ Variable parameter
c-type=1 $ 1: data point, 2: linear, 3: log interpolation
nc=3 $ Number of data points
2.0 2.3 2.8
autorun.inp
Change autorun.inp
file=phits.inp $ PHITS input file name
set:c1 $ Variable parameter
c-type=2 $ 1: data point, 2: linear, 3: log interpolation
nc=5 $ Number of data points
cmin = 2.0
cmax = 2.8
Check the consistency between “outfiles/1” and “eachout/2.0”, … “outfiles/5” and “eachout/2.8”

## Slide 16
Contents
Table of Contents
Make your own script files
Use “autorun.bat/sh”
Use [anatally] and ANOVA
Summary

## Slide 17: What is [anatally] & ANOVA?
Total uncertainty
(0.5553)
Systematic uncertainty
(0.5481)
Statistical error
(0.0894)
[anatally]: Special tally for analyzing multiple tally results based on ANOVA or user-defined function*.
ANOVA (ANalysis Of VAriance): A collection of statistical models for analyzing the differences among the means.
In PHITS, ANOVA is used for evaluating the systematic uncertainty associated with a certain variable (ci) in the input file
c1 | Mean | r.err
2.0 | 4.98e-2 | 0.0636
2.2 | 3.56e-2 | 0.0754
2.4 | 2.67e-2 | 0.1051
2.6 | 1.74e-2 | 0.1215
2.8 | 1.02e-2 | 0.1245
Doses at the end of concrete
ANOVA
*defined in phits/src/usranatal.f. Compilation of PHITS is required when it is changed

## Slide 18: Exercise 8
→ Check “track_rz_anatally.eps”
Delete “$” for the anatally subsection written in [t-track] of phits.inp
Save “phits.inp” and run “autorun.bat” or “autorun.sh” with autorun.inp
phits.inp
Activate anatally function
[ T-track ]
…
angel = ymax(3.0) ymin(0.01)
$ anatally start $ Anatally subsection starts here
$ manatally = 1 $ Type of Anatally (0: user-defined, 1:ANOVA)
$ sfile=track_rz_anatally.out $ Anatally output file name
$ anatally end $ Anatally subsection ends here
After finishing all simulations, “anatally.inp” is automatically created and executed by PHITS, and the results from ANOVA is output in a file specified by “sfile” parameter

## Slide 19: Answer 8
anatally.inp
[parameters]
icntl = 17
…
icntl=17 is for anatally
track_rz_anatally.eps
insensitive to the density
sensitive to the density
track_rz_anatally.out
x: z [cm]
y: effective dose [psv/source]
p: xlin ylog afac(0.8) form(0.9)
p: ymax(3.0) ymin(0.01)
h: n x y1(all ),hh0l ny21 dy1=[y1*y21]
# z-lower z-upper all r.err
0.0000E+00 1.0000E+00 1.9613E+00 0.0221 0.0210 0.0067
1.0000E+00 2.0000E+00 2.0248E+00 0.0230 0.0217 0.0077
…
Mean, total, systematic, statistical uncertainties
Only mean and total uncertainties are shown

## Slide 20: Exercise 9
Simulations only for 3 conditions (mean & mean ± 1σ) are generally sufficient to evaluate the systematic uncertainty*
Evaluate the total uncertainty when the mean and uncertainty of the concrete density is known to be ρ = 2.3 ± 0.1 (g/cm3)
Try three-condition method
*S. Hashimoto and T. Sato, J. Nucl. Sci. Technol. 56, 345 (2019)
autorun.inp
file=phits.inp $ PHITS input file name
set:c1 $ Variable parameter
c-type=2 $ 1: data point, 2: linear, 3: log interpolation
nc=5 $ Number of data points
cmin = 2.0
cmax = 2.8
file=phits.inp $ PHITS input file name
set:c1 $ Variable parameter
c-type=2 $ 1: data point, 2: linear, 3: log interpolation
nc=3 $ Number of data points
cmin = 2.2
cmax = 2.4

## Slide 21: Answer 9
track_rz_anatally.eps
Total uncertainties including systematic uncertainties are not so significant

## Slide 22
Contents
Table of Contents
Make your own script files
Use “autorun.bat/sh”
Use [anatally] and ANOVA
Summary

## Slide 23
Script files can significantly reduce your effort on running PHITS simulations for a variety of conditions
As for the sample script files, you can select either the combination of “eachrun.bat/sh” and “multirun.bat/sh”, or “autorun.bat/sh”
“autorun.bat/sh” is useful particularly when the systematic uncertainties of a certain variable in PHITS input file must be evaluated
Summary