## Slide 1: PHITS
Multi-Purpose Particle and Heavy Ion Transport code System
title
Aug. 2018 revised
Guidance for hands-on exercise
Medical linac
Notes: PHITS講習会 入門実習

## Slide 2: Step 1
Install X-ray generator made of Tungsten
Install X-ray collimator made of Lead
Check the geometry by T-track with axis = xz

## Slide 3
Without (target + collimator)
With (target + collimator)

## Slide 4: Step 2
Score 2D distribution of dose
  Activate [T-deposit] by deleting “off ”
  fill in mesh, x-type …..unit
  XYZ covers, target, collimator and phantom
What does it look like?
Think why vacuum is white
  i.e, why colors appear only in materials

## Slide 5: Dose distribution example

## Slide 6: Step 3
Change to g-show mode
  Change icntl = 8
  See track.eps
Extend the g-show range
  Extend 8 times
Install shielding
  Thickness 10cm
  Concrete (take composition from C:\phits\data\ material.inp)
  Inner dimension
    X: -20 ~ +20, Y: -20 ~ +20, Z: -20 ~ +60

## Slide 7: Step 4
Measure dose
  maxcas = 300 (save CPU time)
  Measure dose in the concrete shielding
  [T-Track] + Effective dose
    Define [T-track] in the backward concrete shielding
    Define effective dose multiplier (set multiplier ID=-202 [AP irradiation])
    Hint is in C:\phits\recommendation\H10multiplier\H10multiplier.inp
    Dose distribution in whole geometry and depth profile

## Slide 9: Step 5
Measure dose beyond 100 cm concrete
  Increase concrete thickness
    Be careful of outer vacuum “999 so 100.0”
  Introduce importance or weight-window

## Slide 10: Step 6
Measure neutron dose
  Turn on photo-nuclear reaction
  Introduce photo-nuclear reaction bias
    pnimul, importance, istdev = -2 or -1