## Slide 1: PHITS
Multi-Purpose Particle and Heavy Ion Transport code System
title
Aug. 2018 revised
Guidance for hands-on exercise
Neutron target
Notes: PHITS講習会 入門実習

## Slide 2: Step 1
Define a beam pipe made of 5 cm-thick Al
Define 10MeV proton beam
  Beam goes through the beam pipe

## Slide 3: Step 2
Install a target station and generate neutrons
  Full-stop length Li
  Attention! : neutron cross section data and transport threshold
proton
neutron

## Slide 4: Step 3
Install moderator, shield and reflector
  Moderator : Outgoing neutron is thermalized
    Neutrons are down scattered by H2O
  Shield : Stop neutrons exiting from target station
    Neutron absorbing elements… Gd or B
  Reflector : Reflect neutrons
    Pb, Be, etc…

## Slide 5
Be reflector
Moderator (H2O)
Beam pipe
B4C shielding

## Slide 6: Step 4
Adjust neutron spectrum
  Observe neutron spectrum
    Take [T-Cross] sample from \phits\tallysample\t-cross\t-cross_reg.inp
  Change moderator material, thickness, etc.
    Increase maxcas if necessary

## Slide 7: Step 5
Improve the statistical uncertainty
  To see the energy spectrum shape
  Split (slice) moderator and use [importance]
    Splitting of reflector is also useful
Find thermal neutron peak
= Make calculation faster

## Slide 8: Step 6
Time and energy spectrum
  Introduce “t-type”, “tmin”, “tmax”, and “nt” in [T-cross]
  tmin ~ 10 ns
  tmax ~ 10^7 ns (10ms)
  Attention: unit of time is “ns” in PHITS
1.6ns – 2.1 ns
1.9ms – 2.5 ms