## Slide 1: PHITS
Multi-Purpose Particle and Heavy Ion Transport code System
title
Aug. 2018 revised
Guidance for hands-on exercise
Detector
Notes: PHITS講習会 入門実習

## Slide 2: Step 0
start.inp is taken from \phits\recommendation\DetectorResponse\DetectorResponse.inp
Show the tally result

## Slide 3: Step 1
Show the geometry
Take tally sample from \phits\tallysample\t-track\t-track.inp
Adjust the view range (in particular Z direction)

## Slide 4: Step 2
Change following parameters and see results
  Source neutron energy
  emin(2) (e.g. emin(2) = 10 )
  Change detector material
    Neutron detector... He-3, U-235 (fission chamber), Li-6, Gd-155
    Are they sensitive to 35 MeV neutrons?
  Detector size (Attention: source is 10cm radius sphere)

## Slide 5
Left : emin(2) = 10
Right : emin(2) = 1.e-10
Why peak disappeared (hint: thermal neutron)

## Slide 6: Step 3
Change neutron source -> photon source
Change detector type (NaI)
See the result

## Slide 7: Step 4
Change following parameters and see results
  Source gamma energy
    If possible, generate efficiency calibration curve (absorption peak efficiency)
  emin(12,13,14) (e.g. emin(12,13,14) = 10 )
    Remember what the change was like when proj = neutron. Why so different?
  Change detector material
    Photon detector... Ge, BGO(BiGeO), etc
    Are they sensitive to 35 MeV gammas?

## Slide 8: Step 5
Let's make a Compton camera
  Source is pencil beam
    1 MeV gamma ray
  Two Si detectors
    Distance 140 cm (Y=100cm, Z =100cm)
    One is downstream detector (Hint: RCC is useful)
  Take [T-deposit2] tally sample from \phits\tallysample\t-deposit2\t-deposit2_reg.inp
  Think how you can improve efficiency
  What happens if you change energy
  Attention! Do not use bias (improtance, weight)