## Slide 1: PHITS
Guidance for hands-on exercise
Environmental radioactivity
Multi-Purpose Particle and Heavy Ion Transport code System
title
1
Oct. 2024 revised

## Slide 2
hundreds meters
10m
Computational approach to efficiently calculate dose contributions from widely distributed environmental radioactivity
f.g.: Dose evaluation inside a building standing on the ground contaminated by Cs-137
Only a few gammas reach the building among a tremendous number of initiated radiations
=> A large number of histories are required to achieve good statistics
Mean free path ~100m
How to compute efficiently ?

## Slide 3: Semi-infinite ground
200m
200m
1m
Evaluation point (10cm radius sphere)
50cm
Soil
Air
200m
Geometry
set:c1[20000] $ World cylinder radius
set:c2[1.0] $ Density of soil g/cm3
...
[ Surface ]
10 sz 100.0 10.0 $ Detection volume
900 pz -50.0 $ Soil depth down to 50 cm
901 pz 0.0 $ Soil surface
902 pz 20000.0 $ Sky top up to 200 m
910 cz c1 $ World cylinder
groundsource.inp
[ Cell ]
10 1 -1.2e-3 -10 $ Detection volume
1 -1.2e-3 -910 901 -902 10 $ Air
2 -c2 -910 900 -901 $ Soil
900 -1 910:-900:902 $ Outer void
z
x

## Slide 4: Semi-infinite ground (continue)
Soil
Source
set:c1[20000] $ World cylinder radius
set:c2[1.0] $ Density of soil g/cm3
...
[ Source ]
totfact = pi*c1*c1 $ per 1 Bq/cm2
s-type = 1
proj = photon
r0 = c1
z0 = -0.5/c2 $ 0.5g/cm2 depth
z1 = -0.5/c2 $ 0.5g/cm2
dir = all $ isotropic
e-type = 28 $ RI soource
ni = 1
137Cs 1.0 $ activity is 1 Bq
groundsource.inp
Uniform plane source in 0.5 g/cm2 cumulative mass depth
Cs-137 in 1Bq/cm2
Distribute in depth even just after the incidence to account initial migration and ground roughness
RI source setting
phits/lecture/advanced/sourceA
Area

## Slide 5: Semi-infinite ground (continue)
1m
Evaluation point : Cell 10
Soil
Air
Tally
groundsource.inp
Ambient dose equivalent
Derive dose by computing the photon fluence in [T-Track] and multiplying the dose conversion coefficinety using “multiplier” function
phits/lecture/advanced/options
[ T-track ]
file = dose.out
mesh = reg
reg = 10
...
multiplier = 1
part = photon
mat mset1
1 (1.0e-6*3600.0 -200)
Conversion coefficient (pSv cm2)
x 10-6*3600 => Sv/h

## Slide 6: Step 1 (Semi-infinite ground)
Let’s execute PHITS with groundsource.inp
Then check
Fluence distribution in wide area (track.eps)
Fluence distribution around the target (track_inside.eps)
In addition, check
Dose value at the evaluation point (dose.out)

## Slide 7: Step 1 (Semi-infinite ground) Result
# num reg volume all r.err
1 10 4.1888E+03 0.0000E+00 0.0000
track.eps
track_inside.eps
dose.out (Line 38)
maxcas=100,000
No gamma reaches to the evaluation point

## Slide 8: Step 1 (Semi-infinite ground) Continued
Increase the histories 10 times (maxcas=1,000,000)
Then check
Fluence distribution in wide area (track.eps)
Fluence distribution around the target (track_inside.eps)
In addition, check
Dose value at the evaluation point (dose.out)

## Slide 9: Step 1 (Semi-infinite ground) Result
track.eps
track_inside.eps
dose.out (Line 38)
maxcas=1,000,000
One gamma reaches the target => Needs much more histories
# num reg volume all r.err
1 10 4.1888E+03 6.2302E-02 1.0000

## Slide 10: Calculation using reflection boundaries
…
…
Infinite
Mirror image
Mirror image
Mirror image
Mirror image
Reflection boundary
Soil
Air
Transport
Radiations reflected at the boundary = Independent radiations injected from mirror regions
Simulation only following radiations injected to the objective region from infinite radiation field => Very efficient
Reflection boundary

## Slide 11: Step 2 (Reflection boundary)
set:c3[1000] $ Reflection box size xy
[ Surface ]
*101 px -0.5*c3
*102 px 0.5*c3
*103 py -0.5*c3
*104 py 0.5*c3
Geometry
Source
[ Source ] off
...
[ Source ]
totfact = c3*c3
s-type = 2
proj = photon
x0 = -0.5*c3
x1 = 0.5*c3
y0 = -0.5*c3
y1 = 0.5*c3
[ Cell ]
…
100 1 -1.2e-3 -910 901 -902 10 #(101 -102 103 -104)
101 1 -1.2e-3 101 -102 103 -104 901 -902 10
…
200 2 -c2 -910 900 -901 #(101 -102 103 -104)
201 2 -c2 101 -102 103 -104 900 -901
Remove “off”
Reflection boundary
Add * in front of surface #
Execute PHITS and check track_inside.eps and dose.out

## Slide 12: Step 2 (Reflection boundary) Result
# num reg volume all r.err
1 10 4.1888E+03 2.0340E-02 0.0648
track_inside.eps
dose.out (Line 38)
Statistics becomes much better even though calculation time becomes a bit longer
Statistics improves with narrower area

## Slide 13: A building standing alone
ｚ
Reflection boundary
Reflection boundary
Buildings aligned in urban area  A building standing alone
How to compute the situation of a building standing alone ?

## Slide 14: A building standing alone (continued)
Reflection boundary
Take a dump for radiations passing through surfaces of the scoring box
Reflection boundary
Scoring box
Dump data = Radiations injected from infinite field
1st step
2nd step
+
External source (Dump data)
Internal source (Internal ground source)
Two-step calculation
T. Furuta, RPD167(2015)392-398

## Slide 15: Step 3 (Obtain dump data)
Reflection boundary
Reflection boundary
Scoring box
[ T-cross ]
file = cross.out
mesh = reg
reg = 1
r-from r-to area
(101 201) (102 202) 1.0
output = current
unit = 1
axis = reg
dump = -8
1 2 3 4 5 6 7 8
Remove “off”
set:c4[800] $ Scoring box size xy
set:c5[1000] $ Scoring box height
[ Surface ]
100 rpp -0.5*c4 0.5*c4 -0.5*c4 0.5*c4 -50 c5
...
[ Cell ]
...
100 1 -1.2e-3 -910 901 -902 10 #(101 -102 103 -104)
101 1 -1.2e-3 101 -102 103 -104 901 -902 10 100
102 1 -1.2e-3 -100 901 10
200 2 -c2 -910 900 -901 #(101 -102 103 -104)
201 2 -c2 101 -102 103 -104 900 -901 100
202 2 -c2 -100 -901
Scoring box
Scoring box
Execute PHITS and check cross.out and cross_dmp.out

## Slide 16: Step 3 (Obtain dump data) Result
2.200000000000000D+01 4.349391048283195D+01 3.999999999997351D+02 … 2.200000000000000D+01 3.999999999990466D+02 2.453495348295788D+02 …
…
1,022,972 gmma-ray data = Radiations scored by 1,000,000 histories
kf-code x y
cross_dmp.out
cross.out (Line 29)
# num area all
1 1.0000E+00 2.2713E+06 0.0027
Number of photons per second injected to the scoring box from infinite field contaminated by Cs-137 in 1 Bq/cm2

## Slide 17: Step 4 (Dump data source)
Scoring box
[ Source ] off
…
[ Source ]
totfact = 2.2713E+06
s-type = 17
file = cross_dmp.out
proj = photon
dump = -8
1 2 3 4 5 6 7 8
Remove “off”
[ T-cross ] off
file = cross.out
…
[ T-product ]
file = source.out
output = source
mesh = xyz
x-type = 2
nx = 100
...
[ Surface ]
…
101 px -0.5*c3
102 px 0.5*c3
103 py -0.5*c3
104 py 0.5*c3
Remove * to make them normal boundary
Copy [T-track] tally with
file=track_inside.out
and modify the contents in red frame
output=source to display source positions
Execute PHITS and check source.eps

## Slide 18: Step 4 (Dump data source) Result
source.eps
Source positions are shown along the scoring box

## Slide 19: Step 5 (External source)
External source (Dump data)
[ Surface ]
50 rpp -248.0 248.0 -248.0 248.0 2.0 498.0
51 rpp -250.0 250.0 -250.0 250.0 0.0 500.0
52 rpp -250.0 250.0 -250.0 250.0 -50.0 0.0
...
[ Cell ]
10 1 -1.2e-3 -10
11 1 -1.2e-3 10 -50
50 3 -0.64 50 -51
20 2 -c2 -910 900 -901 -52
100 1 -1.2e-3 -910 901 -902 51
200 2 -c2 -910 900 -901 52
900 -1 910:-900:902
[ Source ]
totfact = 2.2713E+06
s-type = 17
file = cross_dmp.out
proj = photon
dump = -8
1 2 3 4 5 6 7 8
externalsource.inp
Execute with externalsource.inp and then check track_inside1.eps and dose1.out
Hut made by 2cm wooden walls

## Slide 20: Step 5 (External source) Result
# num reg volume all r.err
1 10 4.1888E+03 1.0774E-02 0.0874
track_inside1.eps
dose1.out (Line 38)

## Slide 21: Step 6 (Internal source)
Internal source (Internal ground source)
[ Surface ]
50 rpp -248.0 248.0 -248.0 248.0 2.0 498.0
51 rpp -250.0 250.0 -250.0 250.0 0.0 500.0
52 rpp -250.0 250.0 -250.0 250.0 -50.0 0.0
...
[ Cell ]
10 1 -1.2e-3 -10
11 1 -1.2e-3 10 -50
50 3 -0.64 50 -51
20 2 -c2 -910 900 -901 -52
100 1 -1.2e-3 -910 901 -902 51
200 2 -c2 -910 900 -901 52
900 -1 910:-900:902
[ Source ]
totfact = c4*c4-500*500
reg = 200
s-type = 2
proj = photon
x0 = -0.5*c4
x1 = 0.5*c4
y0 = -0.5*c4
y1 = 0.5*c4
…
Execute with internalsource.inp and check track_inside2.eps and dose2.out
internalsource.inp
Set source only in reg=200 to account no contamination beneath the hut

## Slide 22: Step 6 (Internal source) Result
track_inside1.eps
dose1.out (Line 38)
# num reg volume all r.err
1 10 4.1888E+03 2.0261E-03 0.1278

## Slide 23: Step 7 (Sumtally)
Internal source (Internal ground source)
External source (Dump data)
+
sumtally.inp
[ T-track ]
file = track_inside.out
…
sumtally start
isumtally = 2
nfile = 2
track_inside1.out 1.0
track_inside2.out 1.0
sfile = track_inside.out
sumfactor = 2.0
sumtally end…
Sumtally subsection
Average track_inside1.out and
track_inside2.out in 1:1
Multiply 2 to obtain sum
Setting of Sumtally
phits/lecture/utility/sumtally
[ Parameter ]
icntl = 13
Execute with sumtally.inp and check track_inside.eps

## Slide 24: Step 7 (Sumtally) Result
track_inside.eps
vdose.eps
Dose distribution in vertical direction in center (1x1m2)
Dose increases with increasing height
=> Higher dose in 2nd floor
# num reg volume all r.err
1 10 4.1888E+03 1.2800E-02 0.0763
dose.out (Line 38)
About a half of dose on infinite ground (2.0340E-02)
Reason of the dose reduction ?

## Slide 25: Step 8 (Shielding effect)
+
External source (Dump data)
Internal source (Internal ground source)
[ Cell ]
…
50 1 -1.2e-3 50 -51
…
internalsource.inp
externalsource.inp
Change wall material and density to air
Execute with externalsource.inp and internalsource.inp
and check dose1.out and dose2.out
Compare to dose inside hut (1.2800E-02Sv/h) and dose on infinite field (2.0340E-02Sv/h)

## Slide 26: Step 8 (Shielding effect) Result
 | External source | Internal source | Total
1. Infinite field | - | - | 2.0340E-02
2. Inside hut | 1.0774E-02 | 2.0261E-03 | 1.2800E-02
3. No wall | 1.1288E-02 | 2.3418E-03 | 1.3630E-02
Reduction factor =
2. Inside hut
1. Infinite field
Shielding factor =
2. Inside hut
3. No wall
＝ 0.63
＝ 0.94
Main reason of dose reduction inside wooden house is not due to shielding effect of the wooden walls but no contamination beneath the house

## Slide 27: Summary
T. Furuta, J. Nucl Sci. Technol. 52(2015)897-904
T. Furuta, Radiat. Prot. Dosim. 167(2015)392-398
Dose calculation in infinite radiation field required for dose evaluation for environmental radioactivity can be performed efficiently using two step calculation with reflection boundary
Two step calculation with reflection boundary
Study of radiation dose reduction of buildings using this method