## Slide 1
1
Guidance for hands-on exercise
Single Event Upset (SEU)
PHITS
Multi-Purpose Particle and Heavy Ion Transport code System
Feb. 2025 revised

## Slide 2
Outline of this exercise
2
Tasks using semiconductor.inp
Step 2: Calculate ion-irradiation on semiconductor device
Step 4: Calculate dependence of SEU cross section
on the energy of incident radiation
Step 1: Edit the geometry of semiconductor device
Tasks using small-satellite.inp
Step 5: Set SEU cross section in [Multiplier] section
Step 6: Calculate SEU rate in small satellite
Step 7: Investigate the effect of thickening
small satellite wall on SEU rate
Step 3: Calculate SEU cross section

## Slide 3
3
Open semiconductor.inp
Check the geometry by PHIG-3D and/or [T-Track] with icntl = 8
500 μm
500 μm
3.0 μm
0.35 μm
2.0 μm
2.0 μm
0.25 μm
Insulation layer (SiO2)
ρ = 2.65 g/cm3
Package layer (Epoxy, C18H19O5)
ρ = 1.85 g/cm3
Silicon substrate (Si)
ρ = 2.329 g/cm3
STI (SiO2)
ρ = 2.65 g/cm3
Metal layer (Cu : SiO2 = 3 : 1)
ρ = 5.69 g/cm3
* mol ratio
Direction of source projectiles
x
y
z
z = 0 μm
0.2 μm
0.1 μm

## Slide 4
Step 1: Edit the geometry
4
500 μm
500 μm
3.0 μm
0.35 μm
2.0 μm
2.0 μm
0.25 μm
Insulation layer (SiO2)
ρ = 2.65 g/cm3
Package layer (Epoxy, C18H19O5)
ρ = 1.85 g/cm3
Silicon substrate (Si)
ρ = 2.329 g/cm3
STI (SiO2)
ρ = 2.65 g/cm3
Metal layer (Cu : SiO2 = 3 : 1)
ρ = 5.69 g/cm3
* mol ratio
Direction of source projectiles
x
y
z
z = 0 μm
0.2 μm
0.1 μm
Sensitive volume (Si)
ρ = 2.329 g/cm3
0.5 μm
Define the sensitive volume (cell 10) in the silicon substrate
Check the geometry by PHIG-3D and/or [T-Track]
[ S u r f a c e ]
21 px -0.05e-4
22 px 0.05e-4
23 py -0.10e-4
24 py 0.10e-4
4 pz 0.00e-4
6 pz 0.50e-4

## Slide 5
Sensitive volume
Sensitive volume
5
[ C e l l ]
…
5 1 -2.329 11 -12 13 -14 5 -7
#(21 -22 23 -24 5 -6)
10 1 -2.329 (21 -22 23 -24 4 -6)

## Slide 6
Step 2: Calculation of ion-irradiation
Define [Source] section to irradiate 4He ions with the energy of 10MeV/n on the device from the package side uniformly and vertically
Change the parameter of [T-Deposit] section to score the variance of deposition energies in the sensitive volume (Cell 10) by individual history
6
Change “icntl=0”, run PHITS and check results

## Slide 7
7
[ S o u r c e ]
s-type = 2
proj = 4He
e0 = 10.0
x0 = -1.0e-4
x1 = 1.0e-4
y0 = -1.0e-4
y1 = 1.0e-4
z0 = -1.0
z1 = -1.0
dir = 1.0
[ T – D e p o s i t ]
mesh = reg
reg = 10
e-type = 1
...

## Slide 8
Step 3: Calculate SEU cross section
Calculate SEU cross sections
Open tdeposit_to_SEUCS_4He.xlsx and select the sheet of “10MeV”
Paste the result of [T-Deposit] on D ~ G columns
SEU cross sections and statistical errors for each critical charge are obtained in K ~ M columns
(*see next slide)
Note:
SEU is occurred when charges collected into sensitive node exceed threshold value (so-called critical charge, Qfit).
[T-Deposit] outputs probability of events for each deposited energy.
Integral of probability from Qfit corresponds to SEU cross section.
Qfit depends on the condition of semiconductor device, so it is useful to calculate Integral of probability from Qfit for each Qfit.
Since PHITS cannot output such values, so external processing using such as Excel is necessary.

## Slide 9
* How to paste each column data of
[T-Deposit] on D ~ G columns of excel file
Notepad++: Hold down the Alt key and mouse drag
(a)
Use “column selection (rectangle selection)” function of text editor, and copy & paste each column data
CotEditor: Hold down Option(Alt) key and mouse drag
(b)
Use “Convert Text to Columns Wizard” of Microsoft Excel
Select the “Data” tab in the ribbon
b-2.
Select the “Text to Columns” in the “Data Tools” group
b-3.
Follow the “Convert Text to Columns Wizard”
b-4.
b-1.
(Ref.) https://support.microsoft.com/en-us/office/split-text-into-different-columns-with-the-convert-text-to-columns-wizard-30b14928-5550-41f5-97ca-7a3e9c363ed7
Paste data on D column and keep highlighting D column
9

## Slide 10
10
Qfit : Critical charge
Ein : Incident energy
sSEU(Ein, Qfit) : SEU cross section
A : Irradiation area
Nin : Number of irradiated particles
Nbit : Number of memory bit
N(Ein, q) : Number of event with
the corrected charge in [q, q+dq]
output of [T-Deposit]

## Slide 11
Step 4: output dependence of SEU cross
sections on incident energy
Calculate SEU cross section for incident energies of 8, 25, 200, 2000 MeV/n
tdeposit_to_SEUCS_4He.xlsx has sheets of “8MeV”, “25MeV”, “200MeV”, “2000MeV” and “10000MeV” to calculate SEU cross section for each incident energy in the same way as the sheet of “10MeV”
11

## Slide 12
12

## Slide 13
13
Open small-satellite.inp
Lens
Image sensor
Transformer
Li-ion
battery
Attitude
control
system
Control boards
Check the geometry by PHIG-3D and/or [T-Track] with icntl = 8

## Slide 14
Step 5: Set [Multiplier] section
14
Set [Multiplier] section to use SEU cross section with the critical charge of 1.0 fC.
When the value of critical charge is set in the cell B8 of the sheet of “SEU_CS”, SEU cross section for each incident energy is obtained in D ~ F columns
(Ref.) How to use multiplier: phits\lecture\advanced\option

## Slide 15
[ Multiplier ]
number = -200
interpolation = log
part = 4He
ne = 5
$ E_in (MeV/u), σ_SEU (cm2/bit)
8.0e+0 0.00e-0
1.0e+1 1.64e-12
2.5e+1 2.00e-13
2.0e+2 8.00e-13
2.0e+3 2.80e-13
log-log interpolation
15
Last data is applied when multiplier does not defined.

## Slide 16
Step 6: Calculate SEU rate
16
* If computational time is too long, please reduce maxcas and maxbch
Modify parameters of 2nd [T-Track] sections to output SEU rate of image sensor (cell 151) and control boards (cell 152, 153, 154)
Change “icntl=0”, run PHITS and check results

## Slide 17
17
Parts | Cell ID | SEU rate (error/s/bit)
Image sensor | 151 | 1.780e-13
Control board 1 | 152 | 1.818e-13
Control board 2 | 153 | 2.056e-13
Control board 3 | 154 | 1.805e-13
[ T - T r a c k ]
mesh = reg
reg = 151 152 153 154
volume
reg vol
151 4.0*4.0*0.1
152 4.0*4.0*0.1
153 4.0*4.0*0.1
154 4.0*4.0*0.1
e-type = 1
ne = 1
0.0 1.0e+6
unit = 1
axis = reg
file = ttrack-reg.out
part = 4He
gshow = 1
epsout = 1
multiplier = all
mat mset1
all (1 -200)
SEU rate (err/s/bit)

## Slide 18
Increase the thickness of small satellite wall and check the effect of SER rate
Step 7: Investigate the effect of thickening
outer wall on SEU rate
18

## Slide 19
 |  | SEU rate (error/s/bit) | 
Parts | Cell ID | Wall thickness: 0.2 cm | Wall thickness: 1.2 cm
Image sensor | 151 | 1.780e-13 | 1.642e-13
Control board 1 | 152 | 1.818e-13 | 1.656e-13
Control board 2 | 153 | 2.056e-13 | 1.904e-13
Control board 3 | 154 | 1.805e-13 | 1.669e-13
Wall volume (cm3) | 76.1 | 584.1
Wall mass (kg) | 0.21 | 1.58
Mass of a 10 cm cube nanosatellite is approximately 1 kg
SEU rate is reduced only about 10% even though the mass of nanosatellite more than doubles
+ 1.37 kg

## Slide 20
Additional exercise (1)
In the calculation of SEU cross section, turn off parameters of nspred and nedisp and check the result
(Please copy the excel file to compare the SEU cross section with the original setting）
20

## Slide 21
Turn on the nspred and nedisp, and then extend the area of semiconductor device and check the SEU cross section
Additional exercise (2)
21

## Slide 22
Calculate SEU cross section with the other incident energies to obtain smooth curve
Do step 1 ~ 6 for the other ions, and then discuss the main cause of SEUs in space
Additional exercise (3)
22